## Slide 1: Exponential Distribution
Think about usually how long it takes for the elevator to arrive.
Most likely, the it frequently comes in a short while and once in a while, it may come pretty late.
In another word, if we want to use a random variable to measure the waiting time for elevator to come, we can say that:
  1. It must be continuous.
  2. Smaller values have larger probability and larger values have smaller probability.

## Slide 2: Exponential Distribution
Usually, exponential distribution is used to describe the time or distance until some event happens.
It is in the form of:
  where x ≥ 0 and μ>0. μ is the mean or expected value.

## Slide 3: Another form of exponential distribution
In this case,
Then the mean or expected value is

## Slide 4: Exponential Distribution and Poisson Distribution
Poisson is a discrete random variable that measures the number of occurrence of some given event over a specific interval (time, distance)
Exponential describes the length of the interval between occurrence.

## Slide 5: Survivor function
f(x)=λexp{−λx}.
The survivor function is showing the probability of X>t
Obtained by
= exp{−λxt}.

## Slide 6: Important: memory less property of Survivor Function
P (X>s+t | x>t) = P (X>s) i.e. the past is immaterial. At all times probability of an event happening in next S seconds is same.
This is important because it tell us the probability of next failure in next T seconds at any given time is constant.
then probability of failure in next time units at any time is 0.5

## Slide 7: Memory less proof.
P(X>s+t)

## Slide 8
Reliability function and failure rate
Reliability function
For a pdf for the time till failure, define:
Probability of surviving at least till age . i.e. that failure time is later than
is the cumulative distribution function.
Failure rate (aka Hazard Rate)
This is failure rate at time given that it survived until time :

## Slide 9
Example: Find the failure rate of the Exponential distribution
Answer:
The reliability is
Failure rate,
Note: is a constant
The fact that the failure rate is constant is a special “lack of ageing property” of the exponential distribution.
- But often failure rates actually increase with age.

## Slide 10: Reliability Block Diagram and Fault Tree Analysis

## Slide 11: Review
Degradation related failures
  Exponential distribution
    Random Variable: Time between failure events
    Reliability computation
    Memoryless property
    Estimating mean time to failure.
Poisson Distribution
  Number of failure events
Poisson is a special case of binomial distribution

## Slide 12: Review- Right censuring testing
Example:
50 components are tested for two weeks. 20 of them fail in this time, with an average failure time of 1.2 weeks.
What is the mean time till failure assuming a constant failure rate?
Answer:
,
mean time till failure is estimated to be
weeks

## Slide 13: System Dependability Models
Reliability Graph
Fault Trees
  Probabilistic fault trees
Reliability Block Diagrams
Timed Failure Propagation Graphs (covered later in the class)

## Slide 14: System Reliability
A system usually consists of components
Each component consists of sub-components
Components may have
  Different reliability
  Different dependencies between them
System reliability is a function of the reliabilities of the (sub-) components and of the relationships between the components

## Slide 15: Problem
For a system consisting of n components
Every component can be in one of the two conditions: working or failed
How many possible combinations of the status of these n components?
How do you calculate the reliability of the system given the probability of each component being working (or failed)?

## Slide 16: RBD – reliability block diagram
Reliability Block Diagram (RBD) is a graphical representation of how the components of a system are connected from reliability point of view.
RBD is used to model the various series-parallel and complex block combinations (paths) that result in system success.
Reliability of the system is derived in terms of reliabilities of its individual components.
The most common configurations of an RBD are the series and parallel configurations.
A system is usually composed of combinations of serial and parallel configurations.
RBD analysis is essential for determining reliability, availability and down time of the system.

## Slide 17: RBD
Reliability Block Diagram helps reliability analysis using a functional diagram to portray and analyze the reliability relationship of components in a system.
Each element of a system is represented by a block that is in some way interconnected with or through the other blocks of the system at a desired level of assembly. The basic relationship between components are depicted as lines that may be:
  Serial: if a single failure results in entire assembly or system failure
  Parallel: if all redundant units failure causes system failure
  Or a combination of these two

## Slide 18: RBD
In a serial system configuration, the elements must all work for the system to work and the system fails if one of the components fails. The overall reliability of a serial system is lower than the reliability of its individual components.
In parallel configuration, the components are considered to be redundant and the system will still cease to work if all the parallel components fail. The overall reliability of a parallel system is higher than the reliability of its individual components.

## Slide 19: RBD - Steps
Define boundary of the system for analysis
Break system into functional components
Determine serial-parallel combinations
Represent each components as a separate block in the diagram
Draw lines connecting the blocks in a logical order for mission success

## Slide 20: Example (serial RBD)
No redundancy
ALL component of the system are needed to make the system function properly
If any one of the components fails, the system fails
Example
Power Unit
Processor
Monitor
System block diagram

## Slide 21: Example (Series RBD)
Reliability Block Diagram
System is composed of n independent serially connected components.
Failure of any component has a cross system effect, i.e., results in failure of the whole system.
R1/1 R2 /2
...
Example
Power Unit
R /
Processor
R /
Monitor
R /
1 1
2 2
3 3
Power Unit
R1 /1
Processor
R2 /2
Monitor
R3 /3

## Slide 22: Example (Series RBD)
Note Reliability R(t) is that failure will occur from t to ∞. = ( failure rate)
  Probability of failure before t: i.e. anytime between [0,t] =1-
R   Rk

## Slide 23: Parallel connections
Probability of failure until time t
  = (1-) (1-)
  Reliability at time t =
  =1- (1-) (1-)
  = +
  = +
  Thus

## Slide 24: Reliability of redundant structures
Redundancy is the duplication of critical components in a system in order to improve reliability.
Redundancy is normally a parallel connection of identical components – can be active or standby
Standby parallel (the redundant component is started when the primary fails.) e.g., telephone switching circuits)
This is done in sequence until no components left
Standby-parallel

## Slide 25: Reliability of active and standby systems
Reliability of active redundant system is same as a parallel connection

## Slide 26: Reliability of standby systems
The standby system does not start operating until the primary unit fails
The system can survive until time t if the primary unit survives until time t or the primary unit fails before time t, but the second unit survives until time t

## Slide 27: Reliability of standby systems
Assuming we are computing the reliability at time t
The two possibilities can be restated as T1 > t or T1 occurs at α < t and T2 > t − α (because the second unit was not started till α)

## Slide 28: Reliability of standby systems
Rs (t) = P (T2 > t |T2 > T1 ) = P (T1 > t) + P (T1 < t ∩ T2 > t)
  T1 and T2 are the failure times of the two units.
  Note that
  P(α< T1 < α+dα) = f 1(α) dα (the definition of cumulative distribution function)
  P(α< T1 < α+dα α)= R ( α) f 1(α) dα
  P (T1 < t ∩ > t) =
  Thus, Reliability of system = R1(t) +

## Slide 29: Fault Tree Analysis
Fault tree analysis is a graphical representation of the major faults or critical failures associated with a product, the causes for the faults, and potential countermeasures. FTA helps identify areas of concern for new system design or for improvement of existing systems. It also helps identify corrective actions to correct or mitigate problems.
FTA can also be defined as a graphic “model” of the pathways within a system that can lead to a foreseeable, undesirable event. The pathways interconnect contributory events and conditions, using standard logic symbols.
Fault tree analysis is useful both in designing new systems, products or services or in dealing with identified problems in existing products/services. As part of process improvement, it can be used to help identify root causes of trouble and to design remedies and countermeasures.

## Slide 30: FTA Operators
And Gate
  The preceding events must all happen to enable the output (parallel RBD connection)
Or Gate
  Either of the two events can lead to the undesirable output (series RBD connection)

## Slide 31: FTA
OR
AND
Hazard
Basic Event1
Basic Event2
Compound EventA
Basic Event5
Basic Event3
Basic Event4
Hazard arises only if basic events 1, 2 and 5 occur AND compound event A occurs.
Compound event A occurs if basic event 3 OR 4 occurs.

## Slide 32: FTA – with probabilities (reliability)
AND
Hazard
Basic Event
Basic Event
Compound Event
Basic Event
Basic Event
Basic Event
P1
P2
P4
P5
P5 x P4 x (P1+P2) x P3
Multiplication because of AND
P1+P2 P3
OR
All events assumed independent in this case.

## Slide 33: History of FTA
FTA was first used by Bell Labs in connection with the safety analysis of the Minuteman missile launch control system in 1961.
Boeing further developed the technique, applying it to the entire Minuteman system and then to commercial aircraft.
Boeing applied FTA as part of a comprehensive safety review of the Apollo system following the launch pad fire on January 27, 1967.
FTA was used in the WASH-1400 study (1976) conducted to review nuclear plant power design and to assure the public that the probability of nuclear accidents was very small. The 3-mile island accident occurred March 28, 1979.

## Slide 34: Example Flight Display
Airport display system
Critical information source
Operator’s Console
Application Servers
Database Servers
Public Displays
Display Client
Network Cpnnection

## Slide 35: Display fault tree
Airport flight departure display
Hazards:
  No display
  Faulty data
Fault trees identify possible causes

## Slide 36: Software and fault trees
Events corresponding to software failure will be present in fault tree
How do we deal with them?
Is event probability a meaningful concept?
What is the probability that the software will fail:
  1?
  0?
  Neither?
Be careful with this — correct approach is to model the operating environment the software will see
Probability is actually the probability of an input vector arising that causes a software fault to manifest itself

## Slide 37: FTA: Summary
Benefits: The primary advantages of fault tree analyses are the meaningful data they produce which allow evaluation and improvement of the overall reliability of the system. It also evaluates the effectiveness of and need for redundancy.
Limitation: The undesired event evaluated must be foreseen and all significant contributors to the failure must be anticipated. This effort may be very time consuming and expensive. Finally, the overall success of the process depends on the skill of the analyst involved.
  Tend to be very large for real systems
  Evolve as insight is gained

## Slide 38: Cut Sets
A cut set is a set of basic events whose simultaneous occurrence insures that the TOP (TOP of the Fault tree) event occurs.
A cut set is minimal if it cannot be reduced without losing its status as a cut set.

## Slide 39: Example
cut sets
{1, 2, 3} , {1, 2} , {1, 3}
minimal cut sets
{1, 2} , {1, 3}
Cut sets are used to simplify reliability computation in complex system.
They can also help find bottlenecks