## Slide 1: Lecture 2 Terminology and concepts
Based on slides and Material from John Knight

## Slide 2: The weakest link
A chain is only as strong as its weakest link...
Ahhhhh
Many things could go wrong:
Attachment could break
Box could break
Chain could break
Etc.

## Slide 3: How to make it dependable?
Decide how strong the chain/box has to be
  Define dependability requirements
Determine how chain/box might fail
  Determine all possible faults that might occur
Buy high quality chain/box so as to avoid defects
  Practice fault avoidance during construction
Fix any broken links that remain
  Practice fault elimination during construction
Cope with broken links you didn’t find or that break
  Practice fault tolerance during operation

## Slide 4: How to make it dependable?
Decide how strong the chain/box has to be
  Define dependability requirements
Determine how chain/box might fail
  Determine all possible faults that might occur
Buy high quality chain/box so as to avoid defects
  Practice fault avoidance during construction
Fix any broken links that remain
  Practice fault elimination during construction
Cope with broken links you didn’t find or that break
  Practice fault tolerance during operation

## Slide 5: How to make it dependable?
Decide how strong the chain/box has to be
  Define dependability requirements
Determine how chain/box might fail
  Determine all possible faults that might occur
Buy high quality chain/box so as to avoid defects
  Practice fault avoidance during construction
Fix any broken links that remain
  Practice fault elimination during construction
Cope with broken links you didn’t find or that break
  Practice fault tolerance during operation

## Slide 6: How to make it dependable?
Decide how strong the chain/box has to be
  Define dependability requirements
Determine how chain/box might fail
  Determine all possible faults that might occur
Buy high quality chain/box so as to avoid defects
  Practice fault avoidance during construction
Fix any broken links that remain
  Practice fault elimination during construction
Cope with broken links you didn’t find or that break
  Practice fault tolerance during operation

## Slide 7: Dependability steps
Decide how strong the chain/box has to be
  Define dependability requirements
Determine how chain/box might fail
  Determine all possible faults that might occur
Buy high quality chain/box so as to avoid defects
  Practice fault avoidance during construction
Fix any broken links that remain
  Practice fault elimination during construction
Cope with broken links you didn’t find or that break
  Practice fault tolerance during operation

## Slide 8: How To Think About Failures
Accidents are very complex:
Do not jump to conclusions
There is unlikely a “root” or single cause
  There are usually many causal factors
Lessons learned must be comprehensive:
Prevent future occurrences of all causal factors
Always investigate failures

## Slide 9: Understand the progression of failures

## Slide 10: The fundamental chain of fault propagation
Error is a fault
Error if detected is an anomaly
Internal faults or connected faults lead to error
Service Outage is a failure

## Slide 11: Step 1 Determine Consequences of Failure
What Happens If The Chain Breaks?
Remember failure is absence of risk , which must be quantified.

## Slide 12: Consequences of Failure
Direct—device fails and causes injury
Indirect—defective support tool leads to device that fails
Combinations of losses:
  Immediate damage to equipment
  Subsequent loss of service
  Subsequent loss of business reputation
  Subsequent law suits

## Slide 13: Hidden Costs of Failure
Some costs of failure are obvious, others not
Ariane V example:
  Obvious:
    Loss of launch vehicle
    Loss of payload
  Not so obvious:
    Environmental cleanup
    Loss of service from payload
    Vehicle redesign
    Increased insurance rates for launches

## Slide 14: Consequences of Failure
Loss of revenue
Software defects : $200 billion/year (SCC)
  Note: recent worms and viruses
  1 hour of downtime costs
    Brokerage: $6,450,000/hr
    Credit card auth 2,600,000/hr
You can search on web about impact of Netflix/amazon outages.

## Slide 15: Step 2 Define the dependability requirements
How Strong Does The Chain Have To Be?

## Slide 16: Dependability requirements
Informal statements are inadequate:
  “System should not fail.”
  “System must be very reliable.”
Need a target so that, if we meet it, system will perform “acceptably”
Need terminology to define requirements

## Slide 17: Terminology of Dependability

## Slide 18: Dependability
Webster
  Dependable: capable of being depended on: RELIABLE
  suitable or fit to be relied on: DEPENDABLE
Rely:
  to be dependent- <the system for which we depend on water>
  to have confidence based on experience- <someone you can rely on>

## Slide 19: dependability
Old: Dependability is the ability to deliver service that can justifiably be trusted
New: The dependability of a system is the ability to avoid service failures that are more frequent and more severe than is acceptable

## Slide 20: dependability
Old: Dependability is the ability to deliver service that can justifiably be trusted
New: The dependability of a system is the ability to avoid service failures that are more frequent and more severe than is acceptable
Why the change? To allow for the possibility of failure yet the system remaining acceptable

## Slide 21: Failure Taxonomy
Correct service is delivered when the service implements the system function.
A service failure, often abbreviated here to failure, is an event that occurs when the delivered service deviates from correct service.
A service fails either because it does not comply with the functional specification, or because this specification did not adequately describe the system function.
A service failure is a transition from correct service to incorrect service, i.e., to not implementing the system function.
The period of delivery of incorrect service is a service outage. The transition from incorrect service to correct service is a service restoration.
The deviation from correct service may assume different forms that are called service failure modes and are ranked according to failure severities

## Slide 22: Failure viewpoints
Failure domain
Detectability of failures
Consistency of failures
Consequences of failure

## Slide 23: Failure Domain
Content failure:
  Supplied service has incorrect information
Timing failure:
  Timing or duration of information incorrect
  Halt failure:
    System halts and remains in fixed state
  Erratic failure:
    Service delivery is erratic

## Slide 24: Detectability And Consistency
Detectability:
  Signaled, unsignaled, false alarm
    False positives, false negatives
Consistency:
  Consistent—incorrect service seen identically by all users
  Inconsistent—incorrect service seen differently by different users, Byzantine failures

## Slide 25: Attributes of Dependability
Reliability
Availability
Safety
Confidentiality
Integrity
Maintainability
Customers must identify the dependability requirements of their system and developers must design so as to achieve them
Requirements: These are properties that might be required of a given system

## Slide 26: Attributes of Dependability
Note this very carefully…
Fault tolerance is not a system requirement or a system property
  It is a mechanism used to provide dependability
Fault tolerance is not a system property

## Slide 27: Reliability
R(t) =Probability that the system will
operate correctly in a specified
operating environment up until time t
System’s ability to provide continuous service
Note that t is important
If a system only needs to operate for ten hours at a time, then that is the reliability target

## Slide 28: Failure Per Demand
Sometimes, the notion of time, t, is not what we need
Some systems are only called to act on demand:
E.g., Protection systems
For such systems, what we need is:
Probability of failure per demand

## Slide 29: Availability
A(t) = Probability that the system will
be operational at time t
Literally, readiness for service
Admits the possibility of brief outages
Fundamentally different concept

## Slide 30: Reliability vs. Availability
They are not the same.....
Example:
A system that fails, on average, once per hour but which restarts automatically in ten milliseconds would not be considered very reliable but is highly available
Availability = 0.9999972

## Slide 31: Nines of Availability
# 9’s | % | Downtime / year | Systems
2 | 99% | ~5000 minutes | General web site
3 | 99.9% | ~500 minutes | Amazon.com
4 | 99.99% | ~50 minutes | Enterprise server
5 | 99.999% | ~5 minutes | Telephone System
6 | 99.9999% | ~30 seconds | Phone switches
Caveats: How measured? What does it mean to be operational?

## Slide 32: Design Tradeoffs
Availability =
MTTF
-------------------- MTTF + MTTR
How to make availability approach 100%?
MTTF  infinity (high reliability)
MTTR  zero (fast recovery)
Need to define maximum repair time
Need to define how Availability is measured
MTTF = Mean Time To Failure
MTTR = Mean Time To Repair

## Slide 33: Subtleties
Which has higher availability?
  Two 4.5 hour outage / year
  1 minute outage / day

## Slide 34: Subtleties
Which has higher availability?
  Two 4.5 hour outage / year -99.89
  1 minute outage / day – 99.999
For an Internet-based company such as EBay or Amazon, which would be more desirable? Why

## Slide 35: Subtleties
Which has higher availability?
  Two 4.5 hour outage / year -99.89
  1 minute outage / day – 99.999
For an Internet-base company such as EBay or Amazon, which would be more desirable? Why
For an autonomous rover?

## Slide 36: Subtleties
Which has higher availability?
  Two 4.5 hour outage / year -99.89
  1 minute outage / day – 99.999
For an Internet-base company such as EBay or Amazon, which would be more desirable? Why
For an autonomous rover?
Need to specify details of acceptable outages

## Slide 37: How to specify availability
Minimum probability of readiness for service
Period over which probability is measured
    Fixed or moving window
Maximum acceptable outage
Time to repair
Minimum sustained operating time

## Slide 38: Specifying Safety
Absence of catastrophic consequences on the users or the environment
Are commercial aircraft “safe”?
  They crash occasionally
  How many crashes are too many?
Are cars “safe”? They crash quite a lot

## Slide 39: Specifying Safety
Absence of catastrophic consequences on the users or the environment
Are commercial aircraft “safe”?
  They crash occasionally
  How many crashes are too many?
Are cars “safe”? They crash quite a lot
40K deaths/yr; 800/week = 2 fully loaded Boeing 747/week

## Slide 40: Define Risk
Risk is defined to be expected loss per unit time
Safety is defined to be an acceptable level of risk:
Risk =  pr(accidenti) x cost(accidenti)
Risk < pre-defined_delta

## Slide 41: Reliability vs. Availability vs. Safety
They are not the same.....
Example:
  A system that is turned off is not very reliable, is not very available,
  but is probably very safe
In practice, safety often involves specific intervention

## Slide 42: Confidentiality
Absence of unauthorized disclosure of information
  Microsoft source code vs. Linux source code
  Web browsing
  Operating systems security model
    Files, memory
  Medical records
  Credit card transaction records
  School grades

## Slide 43: Integrity
Absence of improper system state alterations
  Operating systems:
    Files, memory, network packets
Linux kernel backdoor attempt
Database records
Your bank account
File transfer
Did I really get the right version of software XYZ?
…

## Slide 44: Security is a Dependability Issue
Security is a combination of attributes:
  Integrity
  Confidentiality
  Availability
Under different circumstances, these attributes are more or less important:
  Denial of service is an availability issue
  Exposure of information is a confidentiality issue

## Slide 45: Maintainability
Ability to undergo repairs and modifications

## Slide 46: General Dependability Requirements
Telecommunications:
  Availability, maintainability
Transportation:
  Reliability, availability, safety
Weapons:
  Safety
Nuclear systems:
  Safety

## Slide 47: Attributes of Dependability
Reliability
Availability
Safety
Confidentiality
Integrity
Maintainability
Customers must identify the dependability requirements of their system and developers must design so as to achieve them
Requirements: These are properties that might be required of a given system

## Slide 48: How Much Is Enough?
Dilemma—could we achieve higher dependability:
If more resources were expended on developing a given system then the rate of failure might be reduced. That being the case, should the developers expend all possible resources on developing the system?
For example, formal verification:
 Known to detect defects
 Considered difficult and expensive to apply
 Should its use be required of all systems with large consequences of failure?

## Slide 49: ALARP
As Low As Reasonably Practicable
Three degrees of risk:
 Tolerable (broadly acceptable)
 Unacceptable—has to be reduced
 ALARP region
Carrot Diagram