## Slide 1: TFPG
ISIS/ Vanderbilt University
Nashville, TN
Gabor Karsai + Nag Mahadevan+Abhishek Dubey

## Slide 2: Timed Failure Propagation Graphs
Causal models that describe the system behavior in presence of faults.
Model is a labeled directed graph where
  Nodes represent either failure modes or discrepancies
  Edges between nodes in the graph represent causality
  Edges are attributed with timing and mode constraints on failure propagation.
A discrepancy can be either monitored (attached to an alarm) or unmonitored.
Failure Cascades
Propagation
links
Alarm Allocation
Failure Modes
Discrepancies
Alarms

## Slide 3: Temporal Failure Propagation Graph (TFPG)
Modeling variants
Untimed, causal network (no modes, propagation = [0..inf])
Modal networks: edges are mode dependent
Timed models
Hierarchical component models
Nodes:
Failure modes
Discrepancies
  AND/OR
  Monitored (option)
Edges:
Propagation delay: [min, max]
Discrete Modes (activation)
Example models (#components,#failuremodes,#alarms)
Trivial examples
Simplified fuel system (~30,~80,~100)
Realistic fuel system (~200,~400,~600)
Aircraft avionics (~2000,~8000,~25000) – generated

## Slide 4: Formal Model of TFPG
G = (F;D;E;M; ET;EM;DC)
  F is a nonempty set of failure nodes.
  D is a nonempty set of discrepancy nodes.

## Slide 5: Failure Propagation Semantics
OR propagation
  Node is triggered by any parent
  Propagation time is counted from the last time the edge is activated
  Node must be activated before the end of the activation period
AND propagation
  All parents must be active
  Failure effects are not required to reach the node at the same time
  Activation occur when the last failure effect reaches the node
D1
D3
D4
1,4
A
3,5
B
1,8
A,B
FM1
t=2
t=3
t=7
Activation period
[9,11]  [4,6]  [8,15]
D1
D3
1,4
A
3,5
B
1,8
A,B
FM1
t=2
t=3
t=7
0
6
22
A
B
D4
Activation period
[9,11]  [4,6]  [8,15]
= [9,15]

## Slide 6: Failure propagation semantics
Failure can only reach nodes of AND type only if it already reached all its parents.
For an OR type node v0 and an edge e = (v; v0) , once a failure effect reaches v at time t it must reaches v0 at a time t0 where e. tmin <= t0 - t <= e.tmax
the activation period of an AND alarm v0 is the min/max composition of the activation periods for each link (v; v0)
If the link is deactivated any time during the propagation (because of mode switching), the propagation stops

## Slide 7: TFPG Reasoning
On-line diagnostics:
Input: Sequence of alarms and mode changes
Output: Sequence of sorted and ranked hypotheses containing failure mode(s) that explain the observations (alarms, mode changes)

## Slide 8
TFPG Hypothesis
TFPG Hypothesis - estimation of the current system state.
  Directly, points to failure modes that “best” explain the current set of observed alarms.
  Indirectly, points to failed monitored discrepancies; those with a state that is inconsistent with the (hypothesized) state of the failure modes

## Slide 9: Hypothesis
A hypothetical state is a map that defines node states and the interval at which each node changes its state.
Formally a hypothetical state at time t is a map Ht : V -> {ON, OFF} X RX R
The estimated earliest (latest) time of state change is denoted H(v).terl (H(v).tlat).

## Slide 10: Consistency of Hypothesis

## Slide 11: Hypothesis structure
Structure
  List of possible Failure Modes
  List of alarms in each set ( Consistent (C)/ Inconsistent (IC)/Missing (M) / Expected (E))
  Metrics : Plausibility/ Robustness/ Failure Rate

## Slide 12: TFPG Diagnostics
Algorithm outline:
  Check if new evidence is explained by current hypotheses.
  If not, create a new hypothesis that assumes a hypothetical state of the system consistent with observations
  Rank hypotheses for plausibility and robustness
  Discard low-rank hypotheses, keep plausible ones

## Slide 13: Hypotheses Evaluation Metrics (Rank)
Hypotheses are evaluated based on the following metrics:
Plausibility: reflects the support of a hypothesis based on the current observed alarm state. It answers the question: Which hypothesis to consider?
Robustness: reflects the potential of a hypothesis (evidence) to change based on remaining alarms. It answers the question: When to take an action?
Failure Rate: is a measure of how often a particular failure mode has occurred in the past.

## Slide 14: Discrete (TFPG) Diagnostics - Features
  Multi-fault hypothesis is the default
    Fault state == State of all failure modes/discrepancies
    Reasoner works with sets of failure modes (instead of individual failure modes)
  Robust algorithm: can tolerate missing/inconsistent alarms
    Parsimony principle: Use simplest explanation
  Time-dependent diagnosis
    Reasoner can be asked to recompute diagnosis upon advance of time
  Modal edges: Propagation happens only if edge is enabled (controlled by system mode)
    Diagnosis takes into consideration last propagation effect
  Non-monotonic alarms:
    Alarm retraction triggers a re-computation of the diagnosis
  Intermittent failure modes
    Consequence: alarm/s change to ‘Off’
    Assumption: low frequency intermittents
    Upon alarm changing to ‘Off’, backtrack to last change to ‘On’ and re-evaluate
    Maintain alternate branches (for alarms ‘On’ and ‘Off’)

## Slide 15: Application to Software

## Slide 16: Mapping to Software
(strict semantics required) example, Component-based software construction: Developed for ARINC-653 based systems.
Monitoring the component
  Interfaces (synchronous/asynchronous calls)
  Component state
  Scheduling and timing (WCET)
  Resource usage
Detection:
  Pre/post conditions over call parameters, rates, and component state
  Conditions over timing properties
  Conditions over resource usage (e.g. memory footprint)
  Combinations of the above
System-Level Diagnosis
  Generate causal fault models from the knowledge of component interconnections.
Mitigation: Component Level and System-Level
  Take action given detected anomaly and state of the component
  Actions: restart, initialize, block call, inject value, inject call, release resource, modify state; combination of the above
All of the above are facilitated by model-based software construction techniques.
Notes: Component-based software construction is required to provide structure to the system and increase reusability.

## Slide 17: Example ARINC-653 Component Model
A CORBA Component Model-like layer on top of ARINC-653 abstractions.
Synchronous Interfaces: call/return
  Periodic: time-triggered
  Aperiodic: event-triggered
Asynchronous Interfaces: publish-subscribe
  Periodic: time-triggered
  Aperiodic: event-triggered
Additional Monitoring interfaces
  State: to observe component state variables
  Resource: to monitor resource usage
  Trigger: to monitor execution timing
Built using MICO ORB and
ARINC 653 primitives

## Slide 18: Component Monitoring
Post/Pre condition violations: threshold, rate, custom filter (moving average)
Resource Violations: Deadline
Validity Violation: Stale data on a consumer
Concurrency Violations: Lock Time Outs.
User code violations: reported error conditions from application code.
  ARINC-653 style errors.

## Slide 19: Example: Assembly of 3 components deployed on two partitions
The Sensor component is triggered periodically and it publishes an event upon each activation.
The GPS component subscribes to this event and is triggered periodically to obtain GPS data from the receiver. It publishes its own output event.
The Nav Display component is triggered sporadically via this event and it uses a required interface to retrieve the position data from the GPS component.
Validity(GPS.data_in)<4ms
Delta(Nav.data_in.time)>0
Rate(gps_data_src.data)>1
Specified Monitoring Conditions

## Slide 20: Fault Scenario:
Injected fault such that sensor stops publication

## Slide 21: Modeling Inter-Component Cascading Faults
We don’t. The cascades can be computed from the component assemblies, if the anomaly types and their interactions are known.
Component ‘elements’
  Methods belong to one of these (7)
Fault cascades within component
(A few of the 38 patterns)
Example

## Slide 22: Modeling Intra-Component Cascading Faults
Inter-component propagation is regular – always follows the same pattern
Intra-component propagation depends on the component!  Need to model internal dataflow and control flow of the component.
Note: Could be determined via source code analysis.

## Slide 23: Modeling Intra-Component Cascading Faults

## Slide 24: Integrated Model for GPS Assembly

## Slide 25: Diagnosis Example