## Slide 1: Lecture 11
Safe Programming

## Slide 2: A Brief History of C

## Slide 3: The C Language
Currently, the most commonly-used language for embedded systems
“High-level assembly”
Very portable: compilers exist for virtually every processor
Easy-to-understand compilation
Produces efficient code
Fairly concise

## Slide 4: C History
Developed between 1969 and 1973 along with Unix
Due mostly to Dennis Ritchie
Designed for systems programming
  Operating systems
  Utility programs
  Compilers
  Filters
Evolved from B, which evolved from BCPL

## Slide 5: C History
Original machine (DEC PDP-11) was very small
  24K bytes of memory, 12K used for operating system
Written when computers were big, capital equipment
  Group would get one, develop new language, OS

## Slide 6: C History
Many language features designed to reduce memory
  Forward declarations required for everything
  Designed to work in one pass: must know everything
  No function nesting
PDP-11 was byte-addressed
  Now standard
  Meant BCPL’s word-based model was insufficient

## Slide 7: The Ken Thompson hack
Must read
  http://www.ece.cmu.edu/~ganger/712.fall02/papers/p761-thompson.pdf
he hacked /bin/login to introduce a backdoor.
he did this by hacking the compiler to introduce the backdoor into a binary whenever it detected that it was compiling the login source code.
he also hacked the compiler to introduce the backdoor-producing code into
  The point is most parsers and lexers are compiled using tools that were compiled using tools compiled by …..
  The original compiler 

## Slide 8: The Ken Thompson hack
Must read
  http://www.ece.cmu.edu/~ganger/712.fall02/papers/p761-thompson.pdf
he hacked /bin/login to introduce a backdoor.
he did this by hacking the compiler to introduce the backdoor into a binary whenever it detected that it was compiling the login source code.
he also hacked the compiler to introduce the backdoor-producing code into
  The point is most parsers and lexers are compiled using tools that were compiled using tools compiled by …..
  The original compiler 

## Slide 9: The Ken Thompson hack
Must read
  http://www.ece.cmu.edu/~ganger/712.fall02/papers/p761-thompson.pdf
he hacked /bin/login to introduce a backdoor.
he did this by hacking the compiler to introduce the backdoor into a binary whenever it detected that it was compiling the login source code.
he also hacked the compiler to introduce the backdoor-producing code into
  The point is most parsers and lexers are compiled using tools that were compiled using tools compiled by …..
  The original compiler 

## Slide 10: The Ken Thompson hack
His point was you might think "I don't trust this binary, I'll build it from source"
but now you're in a state of recursive paranoia.
If you don't trust the binary, why do you trust the compiler binary? Y
you don't, so you build the compiler: but why do you trust the compiler binary to produce a trustworthy compiler?

## Slide 11: Anyways now to what's really wrong with C
https://www.radford.edu/ibarland/Manifestoes/whyC++isBad.shtml

## Slide 12: Unintended Interpretations
What does a[-1]*40 do?

## Slide 13: Unintended Interpretations
What does a[-1]*40 do?
It finds some non-intuitive interpretation of “a"[-1] (one which may vary each time the program runs!, and which can't be predicted by the programmer),
then it grabs a series of bits from some place dictated by the wacky interpretation,
it assumes that these bits are meant to be a number (not even a character),
it multiplies that practically-random number by 40, and
then reports the result, all without any hint of a problem.

## Slide 14: Unintended Interpretations
the C array concept is weak and beyond repair” [pg 212]

## Slide 15: Unintended Interpretations
the C array concept is weak and beyond repair” [pg 212]
A language for students should flag advanced or ambiguous constructs as probable typos. For instance, it's not obvious that in i = v[i++], the final value of i is undefined [C++ ARM, p.46]

## Slide 16: Unintended Interpretations
the C array concept is weak and beyond repair” [pg 212]
A language for students should flag advanced or ambiguous constructs as probable typos. For instance, it's not obvious that in i = v[i++], the final value of i is undefined [C++ ARM, p.46]
In Mathematica, two billion plus two billion is four billion. In Java, it's defined to always be -293 million (approx). In C/C++, it's defined to be whatever answer gets returned, and will vary from machine to machine.

## Slide 17: How about JAVA
it is not correct that 4.0*x*0.5 [is the same as] 2.0*x;
while roundoff happens not to be an issue here, there are large values of x for which the first expression produces infinity (because of overflow) but the second expression produces a finite result.

## Slide 18: How about JAVA
it is not correct that 4.0*x*0.5 [is the same as] 2.0*x;
while roundoff happens not to be an issue here, there are large values of x for which the first expression produces infinity (because of overflow) but the second expression produces a finite result.

## Slide 19: How about JAVA
it is not correct that 4.0*x*0.5 [is the same as] 2.0*x;
while roundoff happens not to be an issue here, there are large values of x for which the first expression produces infinity (because of overflow) but the second expression produces a finite result.
And best of all what does the garbase collector do to the program determinism
  Recall you cannot have voter based checks without deterministic behavior

## Slide 20: Back to C++
C++ is a large language, with many features, and requiring many statements in beginner programs whose meaning is inscrutable to the beginner.
(C++ has 68 operators, with 18 levels of precedence;
The C++ standardization committee itself admits [X3J16 92] “C++ is already too large and complicated for our taste.”

## Slide 21: C++ issue – force casting
#include <iostream.h>
class Trouble { };
class Party {
public:
int const numLegs;
Party() : numLegs(4) { } // C++ syntax for init'ing const numLegs as 4.
};
int main() {
Party *invitation = (Party*) (new Trouble());
// Every Party->numLegs is 4, and
// C++'s type system states that invitation is a Party*,
// so surely:
//
cout << "My dog has " << invitation->numLegs << " legs and a tail!" << endl;
return 0;
}

## Slide 22: C++ issue – force casting
#include <iostream.h>
class Trouble { };
class Party {
public:
int const numLegs;
Party() : numLegs(4) { } // C++ syntax for init'ing const numLegs as 4.
};
int main() {
Party *invitation = (Party*) (new Trouble());
// Every Party->numLegs is 4, and
// C++'s type system states that invitation is a Party*,
// so surely:
//
cout << "My dog has " << invitation->numLegs << " legs and a tail!" << endl;
return 0;
}
the order in which classes are declared -- which should change nothing, according to every C++ manual -- can change the output

## Slide 23: So what can you do.
Making C safe..

## Slide 24: String and memory Safety
ISO/IEC TR 24731-1:2007 provides alternative functions for the C Library (as defined in ISO/IEC 9899:1999) that promote safer, more secure programming.
The functions verify that output buffers are large enough for the intended result, and return a failure indicator if they are not.
  Optionally, failing functions call a "runtime-constraint handler" to report the error. Data is never written past the end of an array.
All string results are null terminated. In addition, the functions in ISO/IEC TR 24731-1:2007 are re-entrant: they never return pointers to static objects owned by the function.
ISO/IEC TR 24731-1:2007 also contains functions that address insecurities with the C input-output facilities.
https://github.com/jbenner-radham/libsafec
http://www.drdobbs.com/cpp/the-safe-c-library/214502214

## Slide 25: What does the standard do.
Guard against overflowing a buffer
Do not produce unterminated strings
Do not unexpectedly truncate strings
Provide a library useful to existing code
Preserve the null terminated string datatype
Only require local edits to programs
Library based solution
Support compile-time checking
Make failures obvious
Zero buffers, null strings
Runtime-constraint handler mechanism
Support re-entrant code
Consistent naming scheme
Have a uniform pattern for the function parameters and return type
Deference to existing technology

## Slide 26: Key term – reentrant ocde
A reentrant function does not hold static data over successive calls, nor does it return a pointer to static data. All data is provided by the caller of the function. A reentrant function must not call non-reentrant functions.
Side-effect free
  The function does not affect any state outside the parameters passed and marked as output.

## Slide 27: Non-reentrant function
/* non-reentrant function */
char *strtoupper(char *string)
{
static char buffer[MAX_STRING_SIZE];
int index;
for (index = 0; string[index]; index++)
buffer[index] = toupper(string[index]);
buffer[index] = 0
return buffer;
}

## Slide 28: Reentrant version
/* reentrant function (a poor solution) */
char *strtoupper(char *string)
{
char *buffer;
int index;
/* error-checking should be performed! */
buffer = malloc(MAX_STRING_SIZE);
for (index = 0; string[index]; index++)
buffer[index] = toupper(string[index]);
buffer[index] = 0
return buffer;
}

## Slide 29: Reentrant version
/* reentrant function (a poor solution) */
char *strtoupper(char *string)
{
char *buffer;
int index;
/* error-checking should be performed! */
buffer = malloc(MAX_STRING_SIZE);
for (index = 0; string[index]; index++)
buffer[index] = toupper(string[index]);
buffer[index] = 0
return buffer;
}
Can we do better? What is still the problem

## Slide 30: Modify interface. Caller manages memory
/* reentrant function (a better solution) */
char *strtoupper_r(char *in_str, char *out_str)
{
int index;
for (index = 0; in_str[index]; index++)
out_str[index] = toupper(in_str[index]);
out_str[index] = 0
return out_str;
}

## Slide 31: Thread Safety
A threadsafe function protects shared resources from concurrent access by locks. Thread safety concerns only the implementation of a function and does not affect its external interface.

## Slide 32: Trying to do Better
MISRA – A standard for C for Safety Critical Systems

## Slide 33
See the MISRA ppt in the folder
MISRA- Motor Industry Software Reliability Association
  They recognized that C was the de facto language for coding automotive systems and that these systems are, therefore, vulnerable to C's limitations.
  Rather than mandating the use of a safer language such as Ada, the organization looked at ways to make C safer. [more expensive to train Ada programmers]

## Slide 34: Example Guidelines
In all, MISRA C 2012 has 159 rules
  143 are required and 16 are advisory
  C code claiming conformance must comply with all 143 required rules
Example rules
  Rule 20 (required): All object and function identifiers shall be declared before use.
  Rule 49 (advisory): Tests of a value against zero should be made explicit, unless the operand is effectively Boolean.
  Rule 104 (required): Non-constant pointers to functions shall not be used.
  Rule 16.2 (required): Functions shall not call themselves, either directly or indirectly.
    This means that recursive function calls cannot be used in safety-related systems. Recursion carries with it the danger of exceeding available stack space, which can be a serious error. Unless recursion is very tightly controlled, it is not possible to determine before execution what the worst-case stack usage could be

## Slide 35: So what happened with Toyota

## Slide 36: Tom Koopman
See the slides from Tom Koopman

## Slide 37: Is there something else

## Slide 38: SPARK Ada
See the spark ADA introduction pdf