## Slide 1: Service Level Objectives
Recall failure is the inability to meet service level objectives

## Slide 2: Service Level Objectives
An SLO sets a target level of reliability for the service’s customers. Above this threshold, almost all users should be happy with your service (assuming they are otherwise happy with the utility of the service).
Below this threshold, users are likely to start complaining or to stop using the service.
SLO is expressed as a threshold on a quantitative metric often called as service level indicators

## Slide 3: Service Level Indicators
SLI as the ratio of two numbers: the number of good events divided by the total number of events
Examples
  Number of successful HTTP requests / total HTTP requests (success rate)
  Number of gRPC calls (https://grpc.io/about/) that completed successfully in < 100 ms / total gRPC requests
  Number of search results that used the entire corpus / total number of search results, including those that degraded gracefully
  Number of “stock check count” requests from product searches that used stock data fresher than 10 minutes / total number of stock check requests

## Slide 4: SLI
The SLI ranges from 0% to 100%, where 0% means nothing works, and 100% means nothing is broken.
making all of your SLIs follow a consistent style allows you to take better advantage of tooling: you can write
  alerting logic,
  SLO analysis tools,
  error budget
  calculation, and reports to expect the same inputs: numerator, denominator, and threshold

## Slide 5: SLI
When attempting to formulate SLIs for the first time, you might find it useful to further divide SLIs into SLI specification and SLI implementation:
SLI specification
  The assessment of service outcome that you think matters to users, independent of how it is measured.
  For example: Ratio of home page requests that loaded in < 100 ms

## Slide 6: SLI Implementation is tricky
Ratio of home page requests that loaded in < 100 ms, as measured from the Latency column of the server log.
  This measurement will miss requests that fail to reach the backend.
Ratio of home page requests that loaded in < 100 ms, as measured by probers that execute JavaScript in a browser running in a virtual machine. [from client side]
  This measurement will catch errors when requests cannot reach our network, but may miss issues that affect only a subset of users.
Ratio of home page requests that loaded in < 100 ms, as measured by instrumentation in the JavaScript on the home page itself, and reported back to a dedicated telemetry recording service.
  This measurement will more accurately capture the user experience, although we now need to modify the code to capture this information and build the infrastructure to record it—a specification that has its own reliability requirements.

## Slide 7: Runtime Performance Monitoring
SLI quantification requires runtime monitoring

## Slide 8: Performance Monitoring
Understand the basic terminology of performance monitoring and analysis.
Understand proper methods of monitoring a system’s performance.
Knowledge of the tools that allow you to monitor system performance.
Understand how to analyze the data provided by the monitoring tools.
Understand how to apply the data to improve system performance.
Understand what to tune, and why to tune it.

## Slide 9: General Performance Tuning Rules
Monitor critical systems from day one in order to get a baseline of what “normal” job mixes and performance levels are for each system.
Before making changes to a system configuration, make sure user jobs are not causing problems.
  users running too many jobs, or jobs of an inappropriate size on the system.
A performance problem may be temporary, so you need to think through any changes before you implement them.
  You might also want to discuss proposed changes with other system administrators as a sanity check.

## Slide 10: Terminology
Bandwidth:
  The amount of a resource available. If a highway contains four lanes (two in each direction), each car holds four people, and the maximum speed limit allows 6 cars per second to pass over a line across the road, the “bandwidth” of the road is 24 people per second. Increasing the number of lanes will increase the bandwidth.
Throughput:
  Percentage of the bandwidth you are actually getting. Continuing with the road example, if the cars only hold one person, the protocol is inefficient (not making use of the available capacity). If traffic is backed up due to an accident and only one or two cars per second can pass the line, the system is congested, and the throughput is impacted. Likewise, if there is a toll booth on the road, the system experiences delays (latency) related to the operation of the toll booth.

## Slide 11: Terminology
Utilization:
  How much of the resource was used. It is possible to use 100% of the resource, and yet have 0% throughput (consider a traffic jam at rush hour).
Latency:
  How long it takes for something to happen. In the case of the road example, how long does it take to pay the toll?
Response time:
  How long the user thinks it takes for something to occur.
Knee:
  Point at which throughput starts to drop off as load increases.

## Slide 12: Terminology
Benchmark:
  Set of statistics that (hopefully) shows the true bandwidth and/or throughput of a system.
Baseline:
  Set of statistics that shows the performance of a system over a long period of time.
  Instantaneous data about the system’s performance is rarely useful for tuning the system. But long-term data is not very useful either, as peaks and valleys in the performance graph tend to disappear over time.
  You need to know the long-term performance characteristics, as well as the “spikes” caused by short-lived processes. A good way to obtain long-term (and short-term) information is to run the vmstat command (virtual memory statistics) every five seconds for a 24-hour period. Collect the data points, reduce/graph these data points, and study the results.

## Slide 13: Single System Monitoring

## Slide 14: UNIX Monitoring
ps
top
vmstat
iostat
nfsstat
netstat
mpstat
Process accounting

## Slide 15: Proc File system
> cat /proc/stat cpu 2255 34 2290 22625563 6290 127 456 cpu0 1132 34 1441 11311718 3675 127 438 cpu1 1123 0 849 11313845 2614 0 18 intr 114930548 113199788 3 0 5 263 0 4 [... lots more numbers ...] ctxt 1990473 btime 1062191376 processes 2915 procs_running 1 procs_blocked 0
The very first "cpu" line aggregates the numbers in all of the other "cpuN" lines.
See https://www.centos.org/docs/5/html/5.2/Deployment_Guide/s1-proc-topfiles.html

## Slide 16: Proc File system
> cat /proc/stat cpu 2255 34 2290 22625563 6290 127 456 cpu0 1132 34 1441 11311718 3675 127 438 cpu1 1123 0 849 11313845 2614 0 18 intr 114930548 113199788 3 0 5 263 0 4 [... lots more numbers ...] ctxt 1990473 btime 1062191376 processes 2915 procs_running 1 procs_blocked 0
The very first "cpu" line aggregates the numbers in all of the other "cpuN" lines.
Cpu Line
user: normal processes executing in user mode
nice: niced processes executing in user mode
system: processes executing in kernel mode
idle: twiddling thumbs
iowait: waiting for I/O to complete
irq: servicing interrupts
softirq: servicing softirqs

## Slide 17: Proc File system
> cat /proc/stat cpu 2255 34 2290 22625563 6290 127 456 cpu0 1132 34 1441 11311718 3675 127 438 cpu1 1123 0 849 11313845 2614 0 18 intr 114930548 113199788 3 0 5 263 0 4 [... lots more numbers ...] ctxt 1990473 btime 1062191376 processes 2915 procs_running 1 procs_blocked 0
The very first "cpu" line aggregates the numbers in all of the other "cpuN" lines.
Cpu Line
user: normal processes executing in user mode
nice: niced processes executing in user mode
system: processes executing in kernel mode
idle: twiddling thumbs
iowait: waiting for I/O to complete
irq: servicing interrupts
softirq: servicing softirqs
Q: How do you compute CPU Utilization?

## Slide 18: Proc File system
> cat /proc/stat cpu 2255 34 2290 22625563 6290 127 456 cpu0 1132 34 1441 11311718 3675 127 438 cpu1 1123 0 849 11313845 2614 0 18 intr 114930548 113199788 3 0 5 263 0 4 [... lots more numbers ...] ctxt 1990473 btime 1062191376 processes 2915 procs_running 1 procs_blocked 0
The very first "cpu" line aggregates the numbers in all of the other "cpuN" lines.
The "intr" line gives counts of interrupts serviced since boot time, for each of the possible system interrupts. The first column is the total of all interrupts serviced; each subsequent column is the total for that particular interrupt.

## Slide 19: Proc File system
> cat /proc/stat cpu 2255 34 2290 22625563 6290 127 456 cpu0 1132 34 1441 11311718 3675 127 438 cpu1 1123 0 849 11313845 2614 0 18 intr 114930548 113199788 3 0 5 263 0 4 [... lots more numbers ...] ctxt 1990473 btime 1062191376 processes 2915 procs_running 1 procs_blocked 0
The very first "cpu" line aggregates the numbers in all of the other "cpuN" lines.
The "ctxt" line gives the total number of context switches across all CPUs.
The "btime" line gives the time at which the system booted, in seconds since
the Unix epoch.
The "processes" line gives the number of processes and threads created, which includes (but is not limited to) those created by calls to the fork() and clone() system calls.
The "procs_running" line gives the number of processes currently running on CPUs.
The "procs_blocked" line gives the number of processes currently blocked, waiting for I/O to complete.

## Slide 20: Meminfo
MemTotal: 255908 kB
MemFree: 69936 kB
Buffers: 15812 kB
Cached: 115124 kB
SwapCached: 0 kB
Active: 92700 kB
Inactive: 63792 kB
HighTotal: 0 kB
HighFree: 0 kB
LowTotal: 255908 kB
LowFree: 69936 kB
SwapTotal: 524280 kB
SwapFree: 524280 kB
Dirty: 4 kB
Writeback: 0 kB
Mapped: 42236 kB
Slab: 25912 kB
Committed_AS: 118680 kB
PageTables: 1236 kB
VmallocTotal: 3874808 kB
VmallocUsed: 1416 kB
VmallocChunk: 3872908 kB
HugePages_Total: 0
HugePages_Free: 0
Hugepagesize: 4096 kB
MemTotal — Total amount of physical RAM, in kilobytes.
MemFree — The amount of physical RAM, in kilobytes, left unused by the system.
Buffers — The amount of physical RAM, in kilobytes, used for file buffers.
Cached — The amount of physical RAM, in kilobytes, used as cache memory.
SwapCached — The amount of swap, in kilobytes, used as cache memory.
Active — The total amount of buffer or page cache memory, in kilobytes, that is in active use. This is memory that has been recently used and is usually not reclaimed for other purposes.
Inactive — The total amount of buffer or page cache memory, in kilobytes, that are free and available. This is memory that has not been recently used and can be reclaimed for other purposes.
HighTotal and HighFree — The total and free amount of memory, in kilobytes, that is not directly mapped into kernel space. The HighTotal value can vary based on the type of kernel used.
LowTotal and LowFree — The total and free amount of memory, in kilobytes, that is directly mapped into kernel space. The LowTotal value can vary based on the type of kernel used.
SwapTotal — The total amount of swap available, in kilobytes.
SwapFree — The total amount of swap free, in kilobytes.
Dirty — The total amount of memory, in kilobytes, waiting to be written back to the disk.
Writeback — The total amount of memory, in kilobytes, actively being written back to the disk.
Mapped — The total amount of memory, in kilobytes, which have been used to map devices, files, or libraries using the mmap command.
Slab — The total amount of memory, in kilobytes, used by the kernel to cache data structures for its own use.
Committed_AS — The total amount of memory, in kilobytes, estimated to complete the workload. This value represents the worst case scenario value, and also includes swap memory.
PageTables — The total amount of memory, in kilobytes, dedicated to the lowest page table level.
VMallocTotal — The total amount of memory, in kilobytes, of total allocated virtual address space.
VMallocUsed — The total amount of memory, in kilobytes, of used virtual address space.
VMallocChunk — The largest contiguous block of memory, in kilobytes, of available virtual address space.

## Slide 21: Network Characteristics
/proc/net/dev The dev pseudo-file contains network device status information.
This gives the number of received and sent packets,
the number of errors and collisions
and other basic statistics.
The format is

## Slide 22: Per process information
Per process information is available in /proc/<pid> folder.

## Slide 23: Resource Constraints on Processes
setrlimit
Cgroups
Disk Quota
Linux tc – network management

## Slide 24: Setrlimit/getrlimit/getrusage
http://man7.org/linux/man-pages/man2/getrusage.2.html
http://man7.org/linux/man-pages/man2/getrlimit.2.html (setrlimit and getrlimit)
  Soft limit
  Hard limit

## Slide 25: Control Groups aka “cgroups”
Two basic kernel abstractions:
1) nested groups of processes
2) “controllers” which limit resources

## Slide 26: Cgroup controllers
Cpu
Memory
freezer

## Slide 27: Try out memory controller
sudo apt-get install libcgroup1 cgroup-tools
sudo mkdir /sys/fs/cgroup/memory/foo
echo 50000000 > /sys/fs/cgroup/memory/foo/memory.limit_in_bytes
./myapplication &
echo 3000> /sys/fs/cgroup/memory/foo/cgroup.procs
Note: if a task exceeds its defined limits, the kernel will intervene and, in some cases, kill that task.
Again, when you read the value back, it always will be a multiple of the kernel page size.
So, although you set it to 500 bytes, it's really set to 4 KB:

## Slide 28: OOM Killer
If the task exceeds budget.

## Slide 29: Writing Monitors
Write programs that utilize the kernel counters from /proc and provide periodic statistics.
Issue alerts when degradation is noticed.
Don’ts of monitoring
  Don’t put too heavy a load on monitoring.
  Interesting problems occur if you try to monitor on a set of machines at the same time.
  Read the following paper
Dubey, Abhishek et al. “Compensating for Timing Jitter in Computing Systems with General-Purpose Operating Systems.” 2009 IEEE International Symposium on Object/Component/Service-Oriented Real-Time Distributed Computing (2009): 55-62.

## Slide 30: Identify process shutdowns.
Parent will know about child termination
  SIGCHLD Handler
  Can restart the child
Linux provides another notification mechanism.
  Netlink socket
https://www.systutorials.com/docs/linux/man/7-netlink/
Check out https://github.com/Parrot-Developers/fusion/blob/master/pidwatch/src/pidwatch.c

## Slide 31: Automatic process start and management
Systemd in linux provides the ability to manage and start long running background processes.

## Slide 32: Distributed Monitoring
Elastic-Search
Nagios
Syslog-NG
Splunk
…
https://medium.com/@wbassler23/getting-started-with-prometheus-pt-1-8f95eef417ed
Your homework. Install and try Prometheus as discussed in following article: