## Slide 1: Resilient Distributed Systems
Networking Background
Abhishek Dubey
Fall 2019
Notes: Module 1 and 2

## Slide 2: What is this lecture about
Networking fundamentals
  Protocols
  Sockets
  Routing
  Multicast/Broadcast

## Slide 3: Tracert – example of networked connection

## Slide 4: Network components

## Slide 5: Taxonomy of Communication Networks
Communication networks can be classified according to the way in which nodes exchange information
Communication
Network
Broadcast Communication
Network
Switched Communication
Network
Circuit-Switched
Communication
Network
Packet-Switched
Communication
Network
Datagram
Network
Virtual Circuit
Network
A hybrid of circuits and packets; headers include a circuit identifier established during a setup phase

## Slide 6: Layering
Separation of concerns
  Break problem into separate parts
  Solve each one independently
  Tie together through common interfaces: abstraction
  Encapsulate data from the layer above inside data from the layer below
This allows independent evolution

## Slide 7: Networking Layers - Physical Layer (1)
Service: move information between two systems connected by a physical link
Service Interface: specifies how to send and receive bits
Protocol: coding scheme used to represent a bit, voltage levels, duration of a bit
Examples: coaxial cable, optical fiber links, radio transmitter/receiver

## Slide 8: Networking Layers - Link Layer (2)
Service: enable end hosts to exchange atomic messages with one another
Using abstract addresses (not just direct physical connections)
Perhaps over multiple physical links
But using the same framing (headers, footers)
Possible other services
Arbitrate access to common physical media
Reliable transmission, flow control
Service Interface: send messages to other end hosts; receive messages addressed to end host
Protocols: addressing, routing, Media Access Control (MAC)

## Slide 9: Networking Layers - Network Layer (3)
Service
  Deliver packets to specified inter-network destination
    Inter-network = across multiple layer-2 networks
  Works across networking technologies (e.g., Ethernet + Wifi + 3G)
    No longer the same framing all the way
  Possible other services
    Packet scheduling, priorities
    Buffer management
Service Interface: send packets to specified inter-network destinations; receive packets destined for end host
Protocols: define inter-network addresses (globally unique); construct routing tables

## Slide 10: Networking Layers - Transport Layer (4)
Service:
  Provide end-to-end communication between processes
  Demultiplexing of communication between hosts
  Possible other services:
    Reliability in the presence of errors
    Timing properties
    Rate adaptation (flow control, congestion control)
Service Interface: send message to specific process at given destination; local process receives messages sent to it
Protocol: port numbers, perhaps implement reliability, flow control, packetization of large messages, framing
Examples: TCP and UDP

## Slide 11: Networking Layers - Application Layer (7 – not 5)
Service: any service provided to the end user
Service Interface: depends on the application
Protocol: depends on the application
Examples: Skype, SMTP (email), HTTP (Web), Halo, etc.
What happened to layers 5 and 6?
  Session and Presentation layers
  Part of OSI architecture, but not Internet architecture

## Slide 12: All Networking Layers Together

## Slide 13: Distributed System Communication Depends on Protcol
A protocol is an agreement on how to communicate
Includes
  Syntax: how a communication is specified and structured
    Format of messages sent and received
    Order of messages
  Semantics: what a communication means
    What actions are taken when transmitting, receiving, or when a timer expires

## Slide 14: Example Protocol- IP Service: Best-Effort Packet Delivery
Packet switching
  Divide messages into a sequence of packets
  Each packet (datagram) is dealt with individually
“Best-effort” delivery
  Packets may be lost
  Packets may be corrupted
  Packets may be delivered out of order
  The same packet may be delivered multiple times
source
destination
IP network
Problem
  Many different network technologies
    E.g., Ethernet, WiFi, fiber, Satellite, etc.
  How can you hook them together?
    n x n translations
IP was designed to glue them together
  n translations
  Minimal requirements (datagram)
The Internet is founded on IP
  “IP over everything”

## Slide 15: IP Service: “Best Effort” Suffices
No error detection or correction
  Payload may be corrupted, fragments of a packet might be missing
  Higher-level protocol can provide error checking
Successive packets may not follow the same path
  Not a problem as long as packets reach the destination
Packets can be delivered out-of-order
  Receiver can put packets back in order (if necessary)
Packets may be lost or arbitrarily delayed
  Sender can send the packets again (if desired)
No network congestion control (beyond “drop”)
  Sender can slow down in response to loss or delay

## Slide 16: IP Header: The foundation of Current Computer Communications
Addresses: datagram destination & source
Framing: datagram length
Priority: any special forwarding?
Extensibility: what if we need to tweak/change IP?
Dealing with problems:
  Integrity: is the header what it’s supposed to be?
  Loop avoidance: make sure packets don’t endlessly circulate
  Fragmentation: what if the datagram is too large?
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any) + Padding (if needed)
Payload
IP Header

## Slide 17: IP Packet Header Fields
Version number (4 bits)
  Indicates the version of the IP protocol
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used
Type-of-Service (8 bits)
  Allow packets to be treated differently based on needs
  E.g., low delay for audio, high bandwidth for bulk transfer
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload
Options (if any) + Padding (if needed)

## Slide 18: IP Packet Header Fields (Continued)
Total length (16 bits)
  Number of bytes in the packet
  Maximum size is 65,535 bytes (216 -1)
  … though underlying links may impose smaller limits
Fragmentation: when forwarding a packet, an Internet router can split it into multiple pieces (“fragments”) if too big for next hop link
Fragmentation information (32 bits)
  Packet identifier, flags, and fragment offset
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload
Options (if any) + Padding (if needed)

## Slide 19: Where does Reassemble Happen?
A1: router R2
1000
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 20: Where does Reassemble Happen?
A2: end-host B (receiver)
500
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000

## Slide 21: Where does Reassemble Happen?
A2: correct answer
  Fragments can travel across different paths!
  Why reassemble in network, if it could be further fragmented later?
500
MTU=1000B
MTU=500B
MTU=1000B
Host A
Host B
R1
R2
MTU (Maximum Transfer Unit) = Maximum packet size handled by network
1000
R3
500

## Slide 22: Time-to-Live (TTL) Field (8 bits)
Potentially lethal problem
  Forwarding loops can cause packets to cycle forever
  As these accumulate, eventually consume all capacity
Time-to-live field in packet header
  Decremented at each hop, packet discarded
  if reaches 0
  …and “time exceeded” message is sent to the source
    Using “ICMP” control message; basis for traceroute

## Slide 23: IP Packet Header (cont’d)
Two IP addresses
  Source IP address (32 bits)
  Destination IP address (32 bits)
Destination address
  Unique identifier/locator for the receiving host
  Allows each node to make forwarding decisions
Source address
  Unique identifier/locator for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Payload
Options (if any) + Padding (if needed)

## Slide 24: IP Addresses (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation. E.g, 12.34.158.5:
00001100
00100010
10011110
00000101
12
34
158
5

## Slide 25: Hierarchical Addressing: IP Prefixes
Divided into network (left) & host portions (right)
12.34.158.0/24 is a 24-bit prefix with 28 addresses
  Terminology: “Slash 24”
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5

## Slide 26: IP Address and a 24-bit Subnet Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111111
00000000
255
255
255
0
Address
Mask

## Slide 27: Addressing Hosts in the Internet
The Internet is an “inter-network”
  Used to connect networks together, not hosts
  Needs a way to address a network (i.e., group of hosts)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
LAN = Local Area Network
WAN = Wide Area Network

## Slide 28: Routers
Router consists of
  Set of input interfaces where packets arrive
  Set of output interfaces from which packets depart
  Some form of interconnect connecting inputs to outputs
Router implements
  Forward packet to corresponding output interface
  (Manage bandwidth and buffer space resources)
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
Router

## Slide 29: Forwarding Table
Store a mapping between IP addresses and output interfaces
  Forward an incoming packet based on its destination address
…
…
3
1.2.3.6
1
1.2.3.5
1
2
1.2.3.5
1.2.3.4
1.2.3.4
2

## Slide 30: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward the host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 31: Scalability Improved
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 32: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding entry
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
host
5.6.7.213

## Slide 33: Special-Purpose Address Blocks
Private addresses
  By agreement, not routed in the public Internet
  For networks not meant for general Internet connectivity
  Blocks: 10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
Link-local
  By agreement, not forwarded by any router
  Used for single-link communication only
  Intent: autoconfiguration (especially when DHCP fails)
  Block: 169.254.0.0/16
Loopback
  Address blocks that refer to the local machine
  Block: 127.0.0.0/8
  Usually only 127.0.0.1/32 is used
Limited broadcast
  Sent to every host attached to the local network
  Block: 255.255.255.255/32

## Slide 34: Host Names vs. IP addresses
Host names
  Mnemonic name appreciated by humans
  Variable length, full alphabet of characters
  Provide little (if any) information about location
  Examples: www.cnn.com and bbc.co.uk
IP addresses
  Numerical address appreciated by routers
  Fixed length, binary number
  Hierarchical, related to host location
  Examples: 129.59.15.60 and 192.168.0.1

## Slide 35: Domain Name System (DNS)
Properties of DNS
  Hierarchical name space divided into zones
  Zones distributed over collection of DNS servers
Hierarchy of DNS servers
  Root (hardwired into other servers)
  Top-level domain (TLD) servers
  Authoritative DNS servers
Performing the translations
  Local DNS servers
  Resolver software
You should read up on how DNS’s hierarchical translation works

## Slide 36: Transport Protocols
Provide logical communication between application processes running on different hosts
Run on end hosts
  Sender: breaks application messages into segments, and passes to network layer
  Receiver: reassembles segments into messages, passes to application layer
Multiple transport protocol available to applications
  Internet: TCP and UDP (mainly)
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 37: Internet Transport Protocols
Datagram messaging service (UDP)
  No-frills extension of “best-effort” IP
  Multiplexing/demultiplexing among processes
Reliable, in-order delivery (TCP)
  Connection set-up & tear-down
  Discarding of corrupted packets
  Retransmission of lost packets
  Flow control
  Congestion control
Services not available
  Delay guarantees
  Bandwidth guarantees
  Sessions that survive change-of-IP-address

## Slide 38: UDP
Lightweight communication between processes
  Avoid overhead and delays of ordered, reliable delivery
  Send messages to and receive them from a socket
User Datagram Protocol (UDP; RFC 768 - 1980!)
  IP plus port numbers to support (de)multiplexing
  Optional error checking on the packet contents
    (checksum field = 0 means “don’t verify checksum”)
SRC port
DST port
checksum
length
DATA

## Slide 39: Ports
Need to decide which application gets which packets
Solution: map each socket to a port
Client must know server’s port
Separate 16-bit port address space for UDP and TCP
  (src_IP, src_port, dst_IP, dst_port) uniquely identifies TCP connection
Well known ports (0-1023): everyone agrees which services run on these ports
  e.g., ssh:22, http:80
  On UNIX, must be root to gain access to these ports (why?)
Ephemeral ports (most 1024-65535): given to clients
  e.g. chat clients, p2p networks

## Slide 40: Why Would Anyone Use UDP?
Finer control over what data is sent and when
  As soon as an application process writes into the socket
  … UDP will package the data and send the packet
No delay for connection establishment
  UDP just blasts away without any formal preliminaries
  … which avoids introducing any unnecessary delays
No connection state
  No allocation of buffers, sequence #s, timers …
  … making it easier to handle many active clients at once
Small packet header overhead
  UDP header is only 8 bytes

## Slide 41: Popular Applications That Use UDP
Multimedia streaming
  Retransmitting lost/corrupted packets often pointless - by the time the packet is retransmitted, it’s too late
  E.g., telephone calls, video conferencing, gaming
Simple query protocols like Domain Name System
  Connection establishment overhead would double cost
  Easier to have application retransmit if needed
“Address for bbc.co.uk?”
“212.58.224.131”

## Slide 42: Transmission Control Protocol (TCP)
Connection oriented
  Explicit set-up and tear-down of TCP session
Stream-of-bytes service
  Sends and receives a stream of bytes, not messages
Congestion control
  Dynamic adaptation to network path’s capacity
Reliable, in-order delivery
  TCP tries very hard to ensure byte stream (eventually) arrives intact
    In the presence of corruption and loss
Flow control
  Ensure that sender doesn’t overwhelm receiver

## Slide 43: TCP Support for Reliable Delivery
Sequence numbers
  Used to detect missing data
  ... and for putting the data back in order
Checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
  No error signal sent - recovery via normal retransmission
Retransmission
  Sender retransmits lost or corrupted data
  Timeout based on estimates of round-trip time (RTT)

## Slide 44: Timeout
Timeout
  If haven’t heard anything from receiver, send again
  Problem: for how long do you wait?
    TCP uses function of estimated RTT
Problem: what if no Ack for retransmission?
  TCP (and other schemes) employs exponential backoff
  Double timer up to maximum - tapers off load during congestion

## Slide 45: Multicast

## Slide 46: Multicast Communication
Multipoint communications support communications between more than two hosts
  One-to-many
  Many-to-many
Unlike broadcast, allows a proper subset of hosts to participate
Example standards
  IP Multicast (RFC 1112, standard)

## Slide 47: Multicast Communication
Multicast abstraction is peer-to-peer
  Application-level multicast
  Network-level multicast
    Requires router support (multicast-enabled routers)
    Multicast provided at network protocol level  IP multicast

## Slide 48: Unicast versus Broadcast versus Multicast
A unicast address identifies a single IP interface
A broadcast address identifies all IP interfaces on the subnet
A multicast address identifies a set of IP interfaces
A multicast datagram is received only by those interfaces interested in the datagram (applications wishing to participate in the multicast group)

## Slide 49: Multicast
Transport mechanism and network layer must support multicast
Internet multicast limited to UDP (not TCP)
  Unreliable: No acknowledgements or other error recovery schemes (perhaps at application level)
  Connectionless: No connection setup (although there is routing information provided to multicast-enabled routers)
  Datagram: Message-based multicast

## Slide 50: IP Multicast
IP supports multicasting
    Uses only UDP, not TCP
    Special IP addresses (Class D) identify multicast groups
    Internet Group Management Protocol (IGMP) to provide group routing information
    Multicast-enabled routers selectively forward multicast datagrams
    IP TTL field limits extent of multicast
Requires underlying network and adapter to support broadcast or, preferably, multicast
    Ethernet (IEEE 802.3) supports multicast

## Slide 51: Multicast group addresses
How to identify the receivers of a multicast datagram?
How to address a datagram sent to these receivers?
    Each multicast datagram to carry the IP addresses of all recipients?  Not scalable for large number of recipients
    Use address indirection
      A single identifier used for a group of receivers

## Slide 52: Multicast Address – IPv4
Class D addresses in the range 224.0.0.0 through 239.255.255.255
224.0.0.0 reserved
224.0.0.1 all-host group
224.0.0.2 all-routers group
224.0.0.1 through 224.0.0.255 reserved for routing-protocols
Datagrams destined to any of theses addresses are never forwarded by a multicast router

## Slide 53: Sending and receiving multicast messages
Receiving Multicast Messages
  Create a UDP socket
  Bind it to a UDP port, e.g., 1234
    All processes must bind to the same port in order to receive the multicast messages
  Join a multicast group address
  Use recv or recvfrom to read the messages
Sending Multicast Messages
  You may use the same socket (you used for receiving) for sending multicast messages or you can use any other UDP socket (it does not have to join any multicast group)

## Slide 54: Sending and receiving multicast messages
Receiving Multicast Messages
  Create a UDP socket
  Bind it to a UDP port, e.g., 1234
    All processes must bind to the same port in order to receive the multicast messages
  Join a multicast group address
  Use recv or recvfrom to read the messages
Sending Multicast Messages
  You may use the same socket (you used for receiving) for sending multicast messages or you can use any other UDP socket (it does not have to join any multicast group)
How would you send broadcast messages?

## Slide 55: Multicast issues
Time To Live
  Set TTL for outgoing multicast datagrams (default is 1  local subnet)
Loopback mode
  Enable or disable local loopback of multicast datagrams
  By default loopback is enabled
  A copy of each multicast datagram sent by a process on the host will also be looped back and processed as a received datagram by that host
Port Reuse
  Allow the same multicast application to have several instances running on the same host
  In Java, Port reuse is enabled by default

## Slide 56: Multicast Example
See the associated example.